## Slide 1: Software Defined Networking COMS 6998-8, Fall 2013
Instructor: Li Erran Li (lierranli@cs.columbia.edu)
http://www.cs.columbia.edu/~lierranli/coms6998-8SDNFall2013/
10/29/2013: SDN Traffic Management

## Slide 2: Outline
Announcements
  Nov 5: No class (university holiday)
  Nov 12: guest Lecture on SDN middleboxes by Seyed Kaveh Fayazbakhsh from Stony Brook University
SDN Traffic Management (30 min)
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm (80 min)

## Slide 3: Motivation
Inter-DC WANs bandwidth demand is high
Content distribution both between servers and to end clients
Site replication for geographic locality and bandwidth efficiency
Availability zones: cross-zone replication

## Slide 4: Motivation (Cont’d)
Inter-DC WANs are highly expensive

## Slide 5: Two key problems
Poor efficiency
average utilization over time of busy links is only 30-50%
Poor sharing
little support for flexible resource sharing
Why?
Source: Ming Zhang, MSR

## Slide 6: One cause of inefficiency: lack of coordination
Background traffic
Non-background traffic
Norm. traffic rate
Time (~ one day)
peak before rate adaptation
peak after rate adaptation
> 50% peak reduction
mean
Source: Ming Zhang, MSR

## Slide 7: Another cause of inefficiency: local, greedy resource allocation
MPLS TE (Multiprotocol Label Switching Traffic Engineering) greedily selects shortest path fulfilling capacity constraint
Source: Ming Zhang, MSR

## Slide 8: Local, greedy resource allocation hurts efficiency
Flow | Src → Dst
A | 1→6
B | 3→6
C | 4→6
1
2
3
4
5
6
7
flow arrival order: A, B, C each link can carry at most one flow
MPLS-TE
Source: Ming Zhang, MSR

## Slide 9
1
2
3
5
6
7
1
2
3
5
6
7
Optimal
Local, greedy resource allocation hurts efficiency
flow arrival order: A, B, C each link can carry at most one flow
MPLS-TE
Source: Ming Zhang, MSR

## Slide 10: Poor sharing
Mapping services onto different queues at switches helps, but # services ≫ # queues
(4 - 8 typically)
When services compete today, they can get higher throughput by sending faster
Borrowing the idea of edge rate limiting, we can have better sharing without many queues
(hundreds)

## Slide 11: Outline
SDN Traffic Management
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm

## Slide 12
Why SDN
Status Quo
SDN Approach
Forwarding and control
Separate forwarding hardware
intermixed on a single box
from control software
Manage network as 1000s of
Manage network as a single
individual boxes
fabric
Decentralized, non-
Logically centralized control
deterministic protocols
with traffic engineering
All bits are created equal
Allocate resources based on
application priority
Apps regulated by per-flow
Demand measurement and
TCP “fair” share
resource shaping at the edge

## Slide 13: Challenges
High performance distributed control systems
Inter-operation with legacy networks (other non-SDN sites or the Internet)
Scalable computation of max-min fair allocation among flows with different priority
Congestion-free data plane update
Working with limited switch memory

## Slide 14: Outline
SDN Traffic Management
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm

## Slide 15
B4 Architecture
NCS: Network Control Servers
RAP: Routing Application Proxy
OFC: OpenFlow Controller
OFA: OpenFlow Agent
NCS and switches share
Out of band
control network

## Slide 16
B4 Architecture: Data Plane
OFA
Switch
OFA
Switch
Site A
OFA
iBGP
Switch
OFA
Switch
eBGP
Clusters
Site B
Site C
Google Confidential and Proprietary
OpenFlow Agent (OFA): is a user-level process running on switch hardware
  implement extended OpenFlow to manage the hardware pipeline
  Forward BGP routing packets to OFC, in turn to BGP stack.

## Slide 17
B4 Architecture: Control Plane
Gateway
Site A Controllers
Cental TE
Server
Quagga
Rout
Prox
TE Agent
Paxos
OFC
NCS 2
NCS 3
NCS 1
Google Confidential and Proprietary
Route Proxy: controller app to connect Quagga and OF switches
  BGP/ISIS route updates
  Routing protocol packets
  Interface updates from switches to Quagga

## Slide 18
Hybrid SDN Deployment
Data Center Network
Cluster
Border
Router
EBGP IBGP/ISIS to
remote sites
(not representative of actual topology)

## Slide 19
Hybrid SDN Deployment
Data Center Network
Cluster
Border
Router
EBGP IBGP/ISIS to
remote sites
Quagga
OFC
Paxos
Glue
Paxos
Paxos

## Slide 20
Hybrid SDN Deployment
IBGP/ISIS to
remote sites
Data Center Network
Cluster
Border
Router
EBGP
OFA OFA
EBGP
IBGP/ISIS to remote sites
Quagga OFC
Paxos Glue
Paxos Paxos
OFA OFA

## Slide 21
Hybrid SDN Deployment
Data Center Network
OFA OFA
Cluster OFA OFA
Border
Router
OFA OFA
EBGP
IBGP/ISIS to remote sites
Quagga OFC
Paxos Glue
Paxos Paxos
OFA OFA
● SDN site delivers full interoperability with legacy sites

## Slide 22
Hybrid SDN Deployment
Data Center Network
OFA OFA
Cluster OFA OFA
Border
Router
OFA OFA
EBGP
IBGP/ISIS to remote sites
Quagga OFC
Paxos RCS
Paxos Paxos
OFA OFA
TE Server
● Ready to introduce new functionality, e.g., TE

## Slide 23
Traffic Engineering Architecture

## Slide 24
TE Optimization Problem
● Max-min fair bandwidth allocation to FlowGroups
  ○ FlowGroups: {DC Pairs, priority class}
● FlowGroup’s priority represented by bandwidth function ● HW capabilities constrains solution:
○ Maximum number of paths ○ Splits quantization

## Slide 25
TE Optimization Algorithm
● Max-min fair bandwidth allocation to FlowGroups
● Fill higher priority along shortest paths and then move to longer paths if needed
● Example: FG1 HIPRI, FG2 LOPRI

## Slide 26: Congestion-free update Problem
How to update forwarding plane without causing transient congestion?

## Slide 27: Congestion-free update is hard
initial state
target state
A
B
B
A
A
B
✘
✘
B
A
Source: Ming Zhang, MSR

## Slide 28
In fact, congestion-free update sequence might not exist!

## Slide 29: Idea
Leave a small amount of scratch capacity on each link

## Slide 30
A=2/3
B=2/3
B=2/3
A=2/3
Slack = 1/3 of link capacity ...
B=1/3
B=1/3
A=2/3
B=1/3
A=2/3
B=1/3
Does slack guarantee that congestion-free update always exists?
Init. state
target state
Source: Ming Zhang, MSR

## Slide 31: Yes!
With slack :
we prove there exists a congestion-free update in steps
one step = multiple updates whose order can be arbitrary
It exsits, but how to find it?
Source: Ming Zhang, MSR

## Slide 32: Congestion-free update: LP-based solution
rate variable:
step
flow
path
input: and
output: ...
congestion-free constraint:
∀i,j on a link
link capacity
Source: Ming Zhang, MSR

## Slide 33: Utilizing all the capacity
non-background is congestion-free
background has bounded congestion
using 90% capacity (s = 10%)
using 100% capacity (s = 0%)
Source: Ming Zhang, MSR

## Slide 34: Limited Switch Memory Problem
Commodity switches has limited memory:
today’s OpenFlow switch: 1-4K rules
next generation: 16K rules
How many we need?
50 sites = 2,500 pairs
3 priority classes
static k-shortest path routing [by data-driven analysis]
it requires 20K rules to fully use network capacity
[Broadcom Trident II]
Source: Ming Zhang, MSR

## Slide 35: Hardness
Finding the set of paths with a given size that carries the most traffic is NP-complete
[Hartman et al., INFOCOM’12]
Source: Ming Zhang, MSR

## Slide 36: Heuristic: Dynamic path set adaptation
important ones that carry more traffic and provide basic connectivity
10x fewer rules than static k-shortest path routing
Path selection:
Rule update:
multi-stage rule update
with 10% memory slack, typically 2 stages needed
Observation:
working path set ≪ total needed paths
Source: Ming Zhang, MSR

## Slide 37: Outline
SDN Traffic Management
  Motivation
  Why SDN
  Challenges
  Architecture and Algorithms
  Implementation and Evaluation
  Conclusions and Future Work
Midterm

## Slide 38
SDN Switch with legacy Routing Protocols
● Built from merchant silicon ○ 100s of ports of
nonblocking 10GE ● OpenFlow support
● Open source routing stacks for BGP, ISIS
● Does not have all features ● Multiple chassis per site ○ Fault tolerance
○ Scale to multiple Tbps

## Slide 39
Benefits of Centralized TE
Relative to Shortest Path
Main benefit comes from reduced provisioning for fault tolerance on high priority traffic

## Slide 40
B4 WAN History

## Slide 41
Conclusions and Future Work
● Dramatic growth in WAN bandwidth requirements
○ Existing software/hardware architectures make it impractical to deliver necessary bandwidth globally ● Software Defined Networking: it works and at scale
○ Separation of hardware from software
○ Efficient logically centralized control/management ○ Incremental migration path
● Convergence to public facing WAN

## Slide 42: Questions?