## Slide 1: Wireless Security

## Slide 2: Wireless is Different
Actually, why is wireless different?
Is it different?
Notes: Wireless is, in fact, different, but less so than some people would have you believe. Try to draw people out at this point—make them say why.

## Slide 3: Wireless is Different
The attacker has access to the network that isn’t as constrained by physical location
Your security perimeter is much larger
Traffic can be monitored
Traffic can be injected

## Slide 4: Common Types of Wireless
Cellular—Range 1.5-2km from the nearest antenna
WiFi—range of about 100 meters
Bluetooth—nominal range of 10 meters
NFC (Near-Field Communication)—4 cm range

## Slide 5: Range
All ranges can be limited by terrain, intervening objects, and more
But use of proper antennas can extend the range—important to realize when analyzing security!
Example: the classic Pringles Can WiFi antenna—perhaps 1 km range
Picture from https://www.flickr.com/photos/wmjr/106601670/ by WmJr.

## Slide 6: (How Far Away is that Node?)
If range limits matter, you can’t trust the nominal limits
Use the ultimate limit: the speed of light.
Sets an upper bound on distance
Example: a signal cannot do a round trip of 5 cm each way in less than .16 nanoseconds
  (Grace Hopper used to hand out foot-long pieces of wire and describe them as “nanoseconds”)
(The actual calculation is a bit more complex, but it can only raise that limit)

## Slide 7: Possible Attacker Goals
Host Access: Ability to talk to a given computer on the net
Network Access: Ability to act as a legitimate computer on the wireless net
Content Access: Ability to read packets sent and received
Metadata Access: Ability to conduct traffic analysis

## Slide 8: NFC
Primarily used for payments
  The same basic protocol is used for RFID credit cards
Relatively low bandwidth—106–424K bps
Often used by very low power devices, e.g., RFID chips—hard to do much crypto
Sometimes used to set up faster connections, e.g., between Android phones

## Slide 9: NFC: Attacker Goals
Content access, especially for payment card info
Better yet, spoof a payment for something else
Possibility for some host access for phone-to-phone NFC
  Supported on some Android versions

## Slide 10: NFC—Attacks
Hard; none known in the wild
Timing matters for NFC exchanges
Some MitM and relay attacks have been demonstrated in the lab
More serious issue: bugs in the NFC protocol stack
Complexity leads to insecurity!

## Slide 11: Bluetooth
Used for short range, moderate bandwidth communications
Typical uses: wireless keyboards and mice, headphones, body-area networks, bootstrapping faster communications, etc.
Bandwidth: up to 1.4 Mbps for Bluetooth 5.0; slower for earlier versions
Security issue: pairing
Pairing: how does one Bluetooth device know which other device to connect to and to encrypt to?

## Slide 12: Bluetooth Pairing
Many variants, depending on device type
Fancier devices can require PIN entry
Simpler devices, e.g., headphones, might enter pairing mode when you do something odd such as holding down the power button
A pairwise secret is negotiated; this is used for future associations and communications after successful pairing
Notes: Survey the room on how they’ve paired devices, especially headphones

## Slide 13: Bluetooth Attacks
Many…

## Slide 14: Bluetooth Attacks
Cryptographic flaws
Protocol flaws
  The Bluetooth protocol stack is very complex
Pairing flaws
Implementation flaws
In other words, more or less anything that can go wrong, has…
Notes: Note that we’ll be discussing complexity and implementation issues later in the term

## Slide 15: WiFi
Extremely common
Intended as “wireless Ethernet”—replacement for traditional, high-speed, wired networks
Speed varies with version, range, and WiFi usage in the area, but generally in the 10s of megabits/second.
Today, used far more than originally anticipated, for phones, tablets, IoT, and more

## Slide 16: WiFi Encryption
WiFi had encryption from the very beginning—but it had a long, tortuous history
The goal of the original standard, WEP, is told in its name: “Wired-Equivalent Privacy”
In other words: make the security equal to that of wired Ethernet, no less—but no more
It didn’t succeed…

## Slide 17: WEP
Shared key among all users of a network
No key management—keys were static
Used RC4, a stream cipher, and an unkeyed CRC instead of a MAC
Originally used a 40-bit key, due to US export rules; later raised to 104 bits
Why RC4? Remember the limitations of 1999 hardware—anything better was deemed too expensive, in silicon and in battery power. RC4 is very efficient
But: WEP was a horrible failure as a security mechanism

## Slide 18: MAC versus MAC
MAC: Message Authentication Code, a keyed cryptographic checksum that detects unauthorized modifications to the message
MAC address: Media Access Control address, i.e., an Ethernet address

## Slide 19: WiFi: A Packet Medium
WiFi—like Ethernet and for that matter IP—is packet-oriented
Each packet is an independent message
  Each packet is self-contained
  Packets may be dropped, duplicated, damaged, or reordered
  Any stream-like semantics have to be handled at a higher protocol layer (on the Internet, that’s TCP)
This means that encryption at the WiFi layer has to be packet-oriented
Notes: This slide is for the benefit of those students who have not taken any networking classes

## Slide 20: WiFi and WEP Encryption
Ideally, WiFi would use a block cipher in some suitable mode of operation, e.g., CBC
  (Modes like GCM hadn’t been invented yet)
Stream ciphers assume a reliable underlying byte sequence—but on a packet network, there is no reliable layer larger than a packet
WEP used RC4, a stream cipher, so every packet had to be encrypted independently
RC4 generates a pseudo-random byte stream that is XORed with the plaintext, a byte at a time
Ci := Pi ⊕ Si
but for WEP, this can only be done within a packet

## Slide 21: WiFi and Stream Ciphers
With stream ciphers, it is vital not to reuse a key stream for two different plaintexts
C1,i ⊕ C2,i = P1,i ⊕ Si ⊕ P2,i ⊕ Si = P1,i ⊕ P2,i
If you know one byte, it gives you the other, or you can guess at one plaintext stream and see if it makes the other make sense
To avoid this, WEP used a 24-bit IV that was concatenated with the static key to form a longer effective key
24 bits wasn’t nearly enough, and they didn’t even specify it properly
Notes: This slide may take some discussion, especially the third bullet. The basic attack is >100 years old

## Slide 22: The IV Problem
224 isn’t very many packets—an access point will send that many fairly quickly
The standard didn’t say how IVs were to be selected—and many devices always started at 0 on power-up (which was frequent, since early WiFi cards were removable from laptops)
If an implementation tried to be smart and use random IVs, instead of sequential ones, it would repeat on average every ~5,000 packets (birthday paradox)
The spec didn’t even bar repeated use of the same IV!
It’s worse!

## Slide 23: Packet Injection
Suppose you know the full content of a packet
  How? Send the target machine such a packet
  Ping the target, and get the ping and the reply
  Or induce the target to send you email or visit your website
XOR the known packet against the ciphertext of a WEP-protected WiFi packet
That gives you the Si for the entire packet—use that to create as many new packets as you wish
Many more variations on this game
But it got worse!

## Slide 24: RC4 Isn’t Very Good
RC4 turned out not to be very strong against cryptanalysis
Especially in the context of WEP, it’s easy to crack
Result: breaking into WEP-protected networks is more or less the only widespread use of a cryptanalytic attack in the wild

## Slide 25: WEP Operational Issues
The lack of key management meant that there were no session keys—recovering the WEP key was all you needed for full access
Since everyone in an organization shared the same key, changing it was logistically almost impossible; everyone had to do it at the same time or they’d lose access
Notes: Spend some time discussing how to do this with, say, an organization of ~100 people, some of whom travel

## Slide 26: What Went Wrong with WEP?
The hardware was underpowered
The designers of WEP knew too little about cryptography—using a stream cipher was simply wrong
  They should have tried to find a low-energy block cipher
  At the very least, they could have used a much longer IV; it would have helped against many of the problems, with almost no performance hit
  They should have used a keyed checksum
They left key management to a higher level of the protocol stack, but it was never designed, let alone implemented or adopted
There were no knowledgeable eyes on the entire standardization process
Notes: WiFi and WEP were IEEE standards. Membership is open only to paying organizations, which excluded academics

## Slide 27: Consequences
WEP attacks have been used in the real world
The TJX attack is just one example
Notes: Note that there are others described in Thinking Security

## Slide 28: WEP versus our Threat List
Host Access: Available due to weak checksum and use of a stream cipher
Network Access: Available via the known full packet attack
Content Access: Available due to cryptanalytic weakness
Metadata Access: The source and destination MAC addresses are sent in the clear

## Slide 29: WPA2: WiFi Protected Access
Much stronger than WEP
Uses AES and a real MAC
Two modes: WPA2 Personal, with a single pre-shared key for the network, and WPA2 Enterprise, which has a login and password per user
Still some cryptographic issues—crypto protocol design is hard
Notes: Mention Columbia U Secure

## Slide 30: How Does WPA2 Fare in our Goal Model?
Host Access: Blocked
Network Access: Blocked
Content Access: Blocked
Metadata Access: The source and destination MAC addresses are sent in the clear
But…

## Slide 31: Metadata Access
Who would want to exploit metadata? Remember that it’s MAC addresses, which stay local.
Intelligence agencies love metadata, to see who talks to whom
  They also may have or be able to build a database of MAC addresses
Network operators can track it
  Intrusion detection; marketing (for public WiFi nets)
For pay networks, impersonate someone else’s MAC address and run up their tab

## Slide 32: WPA2 WiFi versus Wired Nets
With wired nets, you have a well-defined perimeter
You also have switch ports to localize misbehavior
  Suppose that an internal machine has been hacked and starts spoofing its MAC address and IP address
  On wired nets (with enterprise-grade managed switches), you can see which physical port the spoofing is coming from
  With WiFi, the attacker could be more than a kilometer away
  Also: switches (mostly) direct to the intended machine; with WiFi, everyone on the same access point will see it
  Similarly, ARP-spoofing without detection is easier
But: the encryption with WPA2 Enterprise is per-user, so other on-net nodes can’t read the WiFi traffic; they can on some wired nets
Notes: Verify that people understand how switches, ARP, etc., work

## Slide 33: Tracking Misbehavior on WiFi
Start from the access point
Using radio direction-finding is harder than you would think—problems with multipath
Blacklist the offending IP and/or MAC addresses and see who complains
That won’t do much good against a serious attacker!

## Slide 34: Should We Worry About This?
“Flaw in billions of Wi-Fi devices left communications open to eavesdropping” (https://arstechnica.com/information-technology/2020/02/flaw-in-billions-of-wi-fi-devices-left-communications-open-to-eavesdroppng/)
When a device disassociates from an access point, remaining traffic is sent encrypted with a key of all zeroes—and it’s possible for the attacker to force disconnects
Is this scary?
Notes: Ask the class

## Slide 35: Not Really
It’s at best access to a bit of content and a bit of metadata
The attacker can’t control what’s made available

## Slide 36: What About Public WiFi?
Encryption is almost never used
If it is used, it’s WPA2 Personal, not Enterprise, so there’s no protection against on-net eavesdroppers
  Remember that most public WiFi nets are used by normal people, not computer geeks
  Asking users to put up with crazy configuration options will not work
What are the risks? The attacker can achieve all of our goals. Is this a serious problem?

## Slide 37: Public WiFi: Content Access
Content is obviously available; use of encryption is mandatory
Better yet, use a VPN, to encrypt all traffic leaving your computer
MAC address metadata is always sent in the clear—but VPNs hide your destination IP addresses
  If your MAC address is sensitive, change it-–you generally can—before connecting to the WiFi network
Is your VPN gateway sensitive? If so, use Tor
  VPN gateway addresses are most likely to be of interest to intelligence agencies

## Slide 38: Public WiFi: Network Access
It’s a public net; no barriers to joining…
Some nets, e.g., in hotels, may restrict access, but via a very low barrier

## Slide 39: Public WiFi: Host Access
Some public WiFi nets prevent hosts from contacting other hosts on the same network, but you can’t count on that
This is the hard question: what is the risk to your computer if you use a public WiFi network?
How do we analyze this? Of course: execution environment

## Slide 40: Execution Environments
Corporate Desktop
Mostly friendly hosts
  But what if some internal host has already been hacked?
Good internal monitoring should detect traffic diversion attempts
A number of services on, to permit collaboration
Attacker goals
  Access rights of this computer
  Data stored on it (but maybe not much)
Public WiFi
Mostly unknown hosts
  Some might be evil
Intercepting traffic is easy
Few externally-facing services are needed—unless you need to talk to a public printer
Attacker goals
  Access rights of this computer, especially after it goes back to the office
  Data stored on it (probably more than at work)
Notes: Corporate desktops have less on the computers themselves, because they usually use a networked drive

## Slide 41: Differences
There are more assets at risk for laptops on public WiFi
  It may be how there is an inside machine that was hacked—it had been an exposed laptop…
For a serious enemy, the odds of an already-hacked inside machine are moderately high
  No incremental risk of attack!
If we can turn off some services when outside—better yet, have them turned off automatically—the risk of attack may be lower outside
If the corporate firewall works well—an assumption!—it can block nasty stuff from “recreational” sites employees might visit
Notes: Mention that employees in hotel rooms often use their laptops for recreation, too, so you want to permit them to go out via the corporate firewall

## Slide 42: Conclusions
The incremental risk to laptops is not high, especially with modern operating systems
Disabling some services automatically is a good idea
Use a VPN
Encourage use of the corporate firewall, even for recreational browsing

## Slide 43: Fake Hotspots
Most devices automatically associate with known nets
  Nets are identified by SSID (Service Set Identifier)
What if an attacker spoofs a known net, corporate or hotspot?
Conclusion: always use bilateral authentication
  Software should always check the validity of the far side’s certificate

## Slide 44: Always-On VPNs?
Can we have an always-on VPN?
  Recall that a proper VPN will reject non-VPN packets
The problem is sign-on—many public hotspots require some sort of sign-on page before they let you out to the Internet
How do you protect the browser that does the sign-on?
Sandbox it?

## Slide 45: A Sandboxed Browser?
Browsers are sandboxed; should they be allowed to bypass the VPN?
But browsers are always sandboxed because of how vulnerable they are
  (Is the sandbox secure?)
And: browsers often have access to stored passwords
What’s needed: a separate browser that’s outside the VPN, with only the passwords needed to connect to networks
PLUS: a VPN that is automatically and always started for all other network connections
That should make public WiFi safe

## Slide 46: Doing Without WiFi?
Should companies just do without public WiFi?
Why do employees travel with laptops? To increase their productivity—they need connectivity
In other words, there is a risk from no WiFi as well

## Slide 47: Cellular Wireless
Cellular service is usually safer
It’s relatively easy, even for high-end hackers, to divert calls to a mobile phone
But data is data, and is sent over IP, which isn’t controlled by SS7
There are still all of the usual IP routing games, but that’s an Internet story, not a cellular one
However…

## Slide 48: IMSI Catchers
Fake base stations (sometimes called “Stingrays”, after one popular model)
Can locate cell phones belonging to targets; can also intercept traffic from them
  But: must be close enough to the target to present a stronger signal than the real base stations
Newer mobile phone protocols authenticate the base station, too
  But: what if the enemy controls the real cellular network?
  In many countries, there are PTT—postal, telegraph, and telephone—ministries, i.e., the phone network is operated by the government
  Or: phone switches can be hacked

## Slide 49: IMSI Catchers: Uses
Primary law enforcement uses:
  Is a given number in a given location?
  What numbers are in that location?
  N.B. Like all base stations, IMSI catchers have a finite radius they can reach, and almost certainly less than a real base station due to lack of a good, high-mounted antenna
Can IMSI catchers wiretap calls? Data? They could for 2G cellular, but that’s old. Can they today? Unknown publicly.
  But: on their home turf, a foreign intelligence agency can play its games on the land side; they don’t need IMSI catchers for that
  What about intelligence agencies operating in other countries? There have been claims about many IMSI catchers around D.C., but no proof

## Slide 50: Attacker Goals: Cellular
Network Access: Trivial
Host Access: Generally blocked by carriers, but not always
Content Access: Encrypted over the air; how strongly is not clear
Metadata Access: Some available via IMSI catchers
Notes: Mention the Jeep attack in the reading

## Slide 51: Is Wireless Safe?
“It depends”
What is your threat model? Who are your enemies, and what are their goals?
Non-cellular nets require proximity, which limits attackers
Cellular networks are safer except when dealing with intelligence agencies
And again: what is the cost of being offline?